## Slide 1: Module VIII - Emergency Vehicle Operations / Safety
Goal
The goal is to have the participant appreciate the necessity of being prepared to drive emergency vehicles. Understanding the need to be mentally and physically prepared to avoid situations that may adversely affect emergency vehicle operations, implement best practices in safety, and develop defensive driving techniques to avoid or reduce the consequences of vehicle collisions.
Notes: Module Goal. The goal is to get your driver prepared for the emergency response.

## Slide 2: Module VIII - Emergency Vehicle Operations / Safety
Objectives
Describe both the physical and mental impact of motivation.
Explain the link between motivation and positive changes in individual behavior.

## Slide 3: Module VIII - Emergency Vehicle Operations / Safety
Objectives (Cont’d)
Outline the actions that must be completed prior to operating an emergency vehicle.
Recognize that emergency response driving is a complex process involving many factors, tasks, and maneuvers.

## Slide 4: Motivation Exercises

## Slide 5: Motivation
Routine
Comfort
Confidence

## Slide 6: Defensive Driving Goals
To maintain the highest level of safety possible.
To be prepared for unexpected situations and conditions which can adversely affect emergency vehicle operation.
To avoid, through effective training and applied practice, unnecessary legal consequences.
Notes: Each driver is responsible for the safety of himself, fellow firefighters and the public. You have to expected the unexpected and train annually.

## Slide 7: Skid Avoidance
The ability to maintain control of the vehicle utilizing defensive driving skills, vehicle controls and to take in account existing road and traffic conditions. These aspects must be coordinated with good handling skills that demonstrate that the driver is capable of detecting, preventing and making a correction that prevents a skid/crash.
Notes: VFIS teaches skid avoidance vs. skid recovery.

## Slide 8: Actions That May Result In Lost Control
Driving too fast for weather, road or tire conditions
Accelerating too hard
Braking inappropriately
Changing direction too abruptly
Tracking a curve at too high a rate of speed
Notes: Example of actions that may result in lost control.

## Slide 9: Preparing to Drive
Route Planning
Driver Readiness
Effective Start-Up Procedures

## Slide 10: Preparing to Drive
Route Planning
  Maximize Response Efficiency
  Minimize Collision Exposure
  Enabling the Emergency Vehicle Driver to Focus on Actual Driving Tasks
  Avoiding Environmental and Construction Hazards

## Slide 11: Preparing to Drive
Driver Readiness
  Fatigue
  Health
  Personal Problems

## Slide 12: Preparing to Drive
Effective Start-Up Procedures
  Circle of Safety Inspection
  Adjustment of Cab Features
  Wearing of Occupant Restraints
  Receive Signal Before Moving

## Slide 13: If another driver fails to give you the right of way…
YOU CAN NOT FORCE IT!
YOU CAN NOT ASSUME IT!
YOU DO NOT HAVE IT!

## Slide 14: Emergency Response Driving
Predicting the predictable
Expect the unexpected
Be prepared for unexpected problems

## Slide 15: Emergency Response Driving
SIPDE System
  Scan
  Identify
  Predict
  Decide
  Execute

## Slide 16: Emergency Response Driving
Five Visual Habits
1. Aim High in Steering
2. Get the Big Picture
3. Keep Eyes Moving, Scan
4. Make Sure the Other Drivers See the Emergency vehicle
5. Identify an Escape Route
PM Fill-In

## Slide 17: Identify Distracted Drivers
Vehicles that may drift over the lane divider or within their own lane
Vehicles traveling at inconsistent speeds
Drivers who are preoccupied with maps, food, cell phones or other technology
Drivers who appear to be involved in conversation with their passenger

## Slide 18: Use of Emergency Lights and Siren
Signal two basic concepts:
1. They notify other drivers that an approaching emergency vehicle is operating in an emergency mode.
2. They request other drivers to yield the right of way to the emergency vehicle in accordance with state and/or local law.

## Slide 19: Make Sure You Are Seen And Heard.
Lights
Sirens
Horns

## Slide 20: Use of Emergency Lights and Siren
RED - Emergency vehicle
  (Fire/EMS) Stop! May also attract
BLUE - Emergency vehicle
  (Law enforcement)
AMBER - Danger/Caution
  Excellent for rear of vehicle
CLEAR
  Good visibility shut off at scene

## Slide 21: Sirens
A mechanical siren produces a spiraling square wave, thus offering a very strong and focused pattern.
Source: Timberwolf Sirens

## Slide 22: Sirens
Electronic sirens are notorious for having dead spots and creating noise pollution without direct sound penetration making them less effective.
Source: Timberwolf Sirens

## Slide 23: “Sirencide”
300 Feet 40 MPH
12 Feet 60 MPH

## Slide 24: Use of Emergency Lights and Siren
Procedures for Use of Siren
  Use When Responding to an Emergency
  Change to Yelp Mode at Least 200’ from Intersection
  High-low Mode is Least Effective
  Use Another Audible Device to Alert Drivers Who Fail to Hear Siren

## Slide 25: Automated Traffic Control Systems
Assist in clearing traffic from an intersection
Annual refresher training in accordance with NFPA 1451
Proceed with caution
Do not assume these systems will give you a green light

## Slide 26: Emergency Dispatch Protocols
Agencies usually have defined response guidelines for the emergency vehicle operator to follow. These may include light & siren usage, response speeds, number of vehicles and other locally specific policies.

## Slide 27: Emergency Dispatch Protocol Example
CAD Entry: Emergency
  Smoke or fire in building
  Outside fire with exposure
  Gas leak inside building
  Haz-Mat Release with persons in distress
  Critical Medical Incident
  Entrapment

## Slide 28: Emergency Dispatch Protocol Example
CAD Entry: Non-Emergency
  Automatic Fire Alarm- no human report of fire or smoke
  Residential Smoke Alarm Sounding- no indication of fire
  Odor report- no symptoms or persons in distress
  Outside fire with no exposure
  Outside gas leak
  Electrical wires arcing
  Haz-Mat (incl. CO) release- no report of persons in distress
  Water leak

## Slide 29: Space Management
Establishing a cushion of safety on all sides of an emergency vehicle is essential to safe operation.

## Slide 30: Defensive Driving
Following Distance
  4 Second Rule at 40 mph or less; 5 Second Rule Above
  40 mph
Rate of Closure
Blind Spots Alongside
Overhead Clearance
Ground Clearance
Bridges
Traffic Closure from Behind

## Slide 31: Rate of Closure-Yielding
Vehicle Speed Outruns Siren’s Effectiveness
Blocked Field of View
Misinterpretation of Direction of Siren Sound
Hearing Impaired Drivers
Inattentive Drivers
Drivers Distracted by Loud Music, Cellular Phone, Kids, Stress, Road Rage
Aggressive Driving
PM Fill-In

## Slide 32: Space Management
Blind Spots Alongside
Overhead Clearance
Ground Clearance
Bridges
Traffic Closure from Behind

## Slide 33: Bridges
Many potential hazards exits on bridges both for drivers and also for workers attempting to make repairs or structural improvements. The exact hazards can vary greatly based on age, locations, limitations, load bearing capacity and weather conditions.
Notes: According to the U.S. Census Bureau statistical abstract, and as of December, 2010, the total number of bridges in the United States is 604,474. Among them,
146, 633 were found to be deficient and obsolete in the year 2010. As of 2010, 69,223 bridges were structurally deficient, and 77,410 bridges were functionally obsolete. The data is based on the National Bridge Inventory

## Slide 34: Bridges – Strong Winds
Strong winds create a problem called “buffeting”. These conditions occur on bridges such as Bay Bridges, through mountain passes and ravines, and when being passed by large trucks. These wind gusts and blasts can cause total loss of vehicle control.
Notes: Discuss how to handle strong gusts of wind while driving:
Reduce speed
Check for oncoming traffic
Adjust lane position
Do not over steer when responding to the gust
Prepare to counter steer
Stay off the brake

## Slide 35: Bridge Limitations - Weight

## Slide 36: Be Aware of Weight Limits

## Slide 37: Bridge Limitations – Width

## Slide 38: Bridges Limitations – Height

## Slide 39: Speed Management
Four important rules:
1. Emergency vehicles must not be driven in excess of the posted speed limits
2. Emergency vehicles must not exceed cautionary speeds
3. Patient Experience
4. Match speed to road conditions
PM Fill-In

## Slide 40: Cautionary Speeds
Example:
  Speed limitations
  around curves
  Posted restrictions going downhill
  Slower speeds on highway ramps, especially cloverleaf design
  Special speed zones such as schools; hospitals; recreation areas; construction; etc.
Notes: Cautionary speeds were designed for passenger cars. Do not exceed cautionary speeds.

## Slide 41: Basic Maneuvers
Steering
  Use Both Hands
  Keep Arms Inside of Vehicle
  Maintain Hands in “3” and “9” Position

## Slide 42: Basic Maneuvers
Braking and Stopping
  Hydraulic – Pump brake pedal
  Air – Firmly and steadily press brake pedal, release if wheels lock
  ABS – Apply firmly and hold down for duration
  Disc vs. Drum - Differences

## Slide 43: Auxiliary Braking Systems
Warning
Do not use the retarders/engine brakes during inclement weather or when the road surfaces are slippery. Using these systems could result in loss of control of the vehicle
Notes: Check the operators manual for specific guidelines on use and how to turn them off.

## Slide 44: Total Stopping Distance
Perception Time/Distance
Reaction Time/Distance
Vehicle Reaction Time/Distance
Vehicle Braking Distance

## Slide 45: Perception Time/Distance
The distance the vehicle travels from the time your eyes see a hazard until your brain recognizes it. Normal time for an alert driver is approximately
¾ of a second.

## Slide 46: Reaction Time/Distance
The distance traveled from the time your brain tells your foot to move from the accelerator until the time your foot pushes the brake pedal.

## Slide 47: Vehicle Reaction Time/Distance
Once the brake pedal is applied the vehicle reaction time will depend on the type and condition of the braking system.

## Slide 48: Vehicle Braking Distance
The distance it takes the vehicle to come to complete stop once you apply the brakes.

## Slide 49: Stopping Distance Factors
Drivers reaction time
Weather and road conditions
Road surfaces
Vehicle weight
Brake conditions
Tire conditions
Speed

## Slide 50: Rules of Thumb
Average reaction time is ¾ second
You can not steer or brake a vehicle unless you have traction
Wet roads double the stopping distance
When you double your speed it takes four times as much distance to stop your vehicle

## Slide 51: Air Brakes
Brake-lag = Added Delay
Add ½ second or more to stopping distance

## Slide 52: Brake Fade
Excessive heat
Gas build up
Reduced friction

## Slide 53: Snub Braking
Low gear
Identify “safe” speed
  Apply brakes firmly for 3 seconds
  Release and coast to “safe” speed
  Repeat until downgrade is complete

## Slide 54: Basic Maneuvers
Backing Up
  Park Intelligently
  Give Audible Notice
  Use a Spotter
  Understand Signals
  Use Side Mirrors
  Check Front Corners
  Maintain Speed Control

## Slide 55: Circle of Safety or Spotter

## Slide 56: Mirrors

## Slide 57: Basic Maneuvers
Lane Changing
  Plan Ahead
  Signal Intention
  Practice Space Management
  Make the Change of Lanes Smoothly

## Slide 58: Basic Maneuvers
Turning
  Always Signal Before Turning
  Whenever Possible Turn from One Proper Lane into Another Proper Lane

## Slide 59: Basic Maneuvers
Passing
  Check Traffic Both Ahead and Behind
  Check Sides and Double Check Blind Spots
  Signal Before Initiating Pass
  Accelerate While Changing Lanes
  Signal Before Returning to the Driving Lane
  Check Mirror Before Returning to the Driving Lane
  Cancel Directional Signal
  Resume Speed

## Slide 60: Basic Maneuvers
Negotiating Intersections
  Scan for Possible Hazards
  Slow Down
  Change Siren Cadence
  Check Options and Avoid Opposing Lane
  Come to a Complete Stop (controlled intersection)
  Establish Eye Contact
  Proceed One Lane at a Time