## Slide 1: Module IX Vehicle Inspections and Maintenance
Goal
To have the participant understand and perform routine maintenance of their emergency vehicles and their role and responsibility in the process.
Notes: Module Goal

## Slide 2: Module IX Vehicle Inspections and Maintenance
Objectives
Explain the value and importance of regular vehicles inspections.
Identify the major component systems of an emergency vehicle.
Describe how to perform pre- and post-trip inspections.

## Slide 3: Module IX Vehicle Inspections and Maintenance
Objectives (Cont’d)
List the three types of preventive maintenance.
Explain the role of the emergency vehicle driver in performing certain vehicle inspections and maintenance functions.
Describe the importance of keeping accurate and complete records.

## Slide 4: Emergency Vehicle Components
Chassis
Body
Primary Function Components (task or mission)
Auxiliary Systems

## Slide 5: Emergency Vehicle Components
Chassis
  Frame
  Suspension System
  Steering and Braking Systems
  Power Train Components

## Slide 6: Emergency Vehicle Components
Body
Primary Function
Auxiliary Systems

## Slide 7: Inspections
Post-Trip
  Cleaning of Vehicle
  Replacing Supplies
  Inventory Equipment
  Re-fueling and Checking Fluid Levels, If Justified
  Report Any Unusual Occurrences or Malfunctions
PM Fill-In

## Slide 8: Inspection Checklist
Pre-trip
  Vehicle Overview
  Check the Engine Compartment
  Start Engine and Check Inside Cab
  Check Headlights, Signal Lights, Warning Lights, and Audio Devices
  Conduct Walk Around Inspection
  Check Controls and Indicators
  Check Brake System (air brakes)

## Slide 9
PRE-TRIP INSPECTION
CHECKLIST
Notes: New

## Slide 10: Pre-Trip Inspection Checklist
Vehicle Overview
  Look at general condition
  Check windshield for damage and it is clean
  Look for damage and whether the vehicle is leaning
  Check under the vehicle for fresh oil, coolant, grease or fuel leaks
  Review vehicle log
Notes: New

## Slide 11: Pre-Trip Inspection Checklist
Check engine compartment
  Verify parking brake is engaged
  Check engine oil level
  Coolant level and condition of hoses
  Power steering fluid
Notes: New

## Slide 12: Pre-Trip Inspection Checklist
Check engine compartment (cont’d)
  Windshield washer fluid
  Belts for tightness and wear
  Leaks in engine compartment
  Battery fluid level and connections
  Automatic transmission fluid level
Notes: New

## Slide 13: Pre-Trip Inspection Checklist
Start engine
  Listen for noises
  Verify gauges are within normal ranges
    Check any warning lights and/or buzzers
Notes: New

## Slide 14: Pre-Trip Inspection Checklist
Check gauges & warning lights
  Coolant temp. gauge
  Voltmeter
  Tachometer
  Speedometer
  Fuel level gauge
  Transmission oil temp
  Compound air pressure
Notes: New

## Slide 15: Pre-Trip Inspection Checklist
Check inside cab
  Check operations of vehicle controls
    Steering wheel
    Accelerator
    Brakes (parking, service, secondary braking system)
    Transmission
Notes: New

## Slide 16: Pre-Trip Inspection Checklist
Check inside cab (Cont’d)
  Check operations of vehicle controls (Cont’d)
    Horn(s)
    Windshield wiper/washer
    Light switches and indicators
    Mirrors
    Seat adjustments/seatbelts
Notes: New

## Slide 17: Pre-Trip Inspection Checklist
Check headlights, signal lights, warning lights and audio devices
  Running, parking and brake lights
  Turn signals and four-way flashers
  Headlights (low and high beams)
  Warning lights
  Work lights (front, rear, intersection, side and others)
Notes: New

## Slide 18: Pre-Trip Inspection Checklist
Conduct walk-around inspection
  Left front wheel and tire for condition, tread and inflation and the left front suspension
  Windshield, wipers, washer, front bumper and cleanliness of audio devices, lamps and reflectors
  Right front wheel and tire for condition, tread and inflation and the right front suspension
Notes: New

## Slide 19: Pre-Trip Inspection Checklist
Conduct walk-around inspection (Cont’d)
  Cab doors and closure, vehicle body, special body provisions such as pump panel, patient compartment door, equipment and storage compartments and doors
  Right rear wheels and tires for condition, tread and inflation and the right rear suspension
Notes: New

## Slide 20: Pre-Trip Inspection Checklist
Conduct walk-around inspection (Cont’d)
  Hose bed, rear patient compartment doors and other body features (specific to the vehicle being inspected), lamps and reflectors
  Left rear wheel and tire for condition, tread and inflation and the left rear suspension and fuel fill
Notes: New

## Slide 21: Pre-Trip Inspection Checklist
Conduct walk-around inspection (Cont’d)
  All compartments and cab doors, all closures, vehicle body
  Operator’s position specific to the vehicle being inspected such as pump pane. capes, valves, drains and equipment
Notes: New

## Slide 22: Pre-Trip Inspection Checklist
Check controls and indicators at operator’s position or any other or any other special function, components, wherever located
  Check engine controls and indicators, pump controls and indicators, pump panels lights and other controls specific to the vehicle being checked.
Notes: New

## Slide 23: Pre-Trip Inspection Checklist
Check brake system (air brakes)
  Test low pressure warning signal
  Check to ensure that spring brakes come on automatically
  Check the rate of air pressure buildup
  Test the air leakage rate
  Test the parking brake
  Test the service brake
Notes: New

## Slide 24: Pre-Trip Inspection Checklist
Fixed equipment
  Cab lift controls
  Ladder controls
  Cable reels
  Radio equipment
  Other permanently affixed items
Notes: New

## Slide 25: Fixed Equipment
Notes: New

## Slide 26: Practical Application
Time to get up and moving…
Provided a copy of vehicle checklist
Demonstrate vehicle check…
Notes: New- Exercise

## Slide 27: Preventive Maintenance Benefits
Safety
Costs
Operational Effectiveness
Liability
Basis for Purchasing Decisions

## Slide 28: Types of Preventive Maintenance
Routine Maintenance
Scheduled Maintenance
Crisis Maintenance
PM Fill-In

## Slide 29: Types of Preventive Maintenance
Routine
  Fluid Level Checks
  Wheels and Tires
  Electrical Systems and Devices

## Slide 30: Types of Preventive Maintenance
Scheduled
  Manufacturer’s Recommended Schedule
  Amount of Use (example: Regeneration Process)
  Organizational Policy
  Professional Standards

## Slide 31: Types of Preventive Maintenance
Crisis
  Classification A (immediate)
  Classification B (as soon as possible)
  Classification C (next P.M.)
PM Fill-In

## Slide 34: Role of the Emergency Vehicle Driver
Battery or Batteries
Braking System
Coolant System
Electrical System
Fuel
Hydraulic Fluids

## Slide 35: Role of the Emergency Vehicle Driver
Lubrication
Oil (engine)
Tires
Steering System
Belts
Tools, Appliances, and Equipment

## Slide 36: Role of the Emergency Vehicle Driver
Document the need for maintenance on the assigned vehicle
Verify that the requested and needed maintenance was performed
Follow established departmental guidelines for taking the vehicle out of service

## Slide 37: NFPA 1911 Out of Service Criteria
A. Identify apparatus out of service
  Sign on outside of door
  Special bag that covers steering wheel
  Large sign on driver’s window

## Slide 38: NFPA 1911 Out of Service Criteria (Cont’d)
B. Identify components out of service
  Distinctive color sign located on the inside of the driver’s door identifying which component
  Highly visible device provided at the components control(s)

## Slide 39: NFPA 1911 Out of Service Criteria (Cont’d)
C. Driving and Crew Area
  Cracked or broken windshield
  Missing or broken door latches
  Seats without seatbelts, damaged seatbelts, or missing or broken buckles
  Broken wipers or foot throttle

## Slide 40: NFPA 1911 Out of Service Criteria (Cont’d)
D. Chassis, suspension driveline, wheels and axles
  GAWR that exceeds manufacturer’s load rating for any tire
  Weight that exceeds the GAWR for that axle
  Actual overall weight that exceeds GVWR or GCWR

## Slide 41: NFPA 1911 Out of Service Criteria (Cont’d)
D. Chassis, suspension driveline, wheels and axles
  Tires with cuts to the cords
  Front tires with less than 4/32 – inch tread or rear tires with less than 2/32 – inch tread at two adjacent major tread grooves anywhere on the tire
  Wheels or rims damaged
  Weld cracks

## Slide 42: NFPA 1911 Out of Service Criteria (Cont’d)
E. Engine systems
  Engines that won’t crank or start
  Engines that are overheating
  Leaking of fuel
  Excessive leaking of oil
  Oil that contains coolant
  Oil that is diluted with fuel
  Stop-engine light that fails to turn off

## Slide 43: NFPA 1911 Out of Service Criteria (Cont’d)
F. Engine cooling system
  Coolant system leak
  Coolant that contains oil
  Cooling system that exceeds max. operating temperature

## Slide 44: NFPA 1911 Out of Service Criteria (Cont’d)
G. Transmission and clutch
  Automatic transmission that overheats in any range
  Automatic transmission that has a “do not shift” light on
  Transmission components that are leaking transmission oil

## Slide 45: NFPA 1911 Out of Service Criteria (Cont’d)
H. Low voltage and line voltage
electrical systems
  Legally required lighting or horn not operational
  Ignition system not operational
  Charging system not operational
  Failure of warning lights that creates any position around the apparatus from which no warning light is visible
  Inoperative siren (OOS for emergency response)
  Damaged receptacles or other observed shock hazards

## Slide 46: NFPA 1911 Out of Service Criteria (Cont’d)
I. Braking Systems (Air)
  Service brakes that have a air pressure drop of more than 2 psi in 1 min. or a straight chassis or more than 3 psi in 1 min. for a combination chassis, with the engine stopped and the service brake released.
  Brakes that are out of adjustment
  ABS warning indicator (light) activated

## Slide 47: NFPA 1911 Out of Service Criteria (Cont’d)
I. Braking Systems (Air) (Cont’d)
  Braking systems that are not operational
  Air compressor that fails to build up pressure in accordance with manufacturer’s min. specifications
  Air compressor failure to maintain 80 to 90 psi pressure in accordance with manufacturer’s min. specifications
  Brake shoes or disk brake pads that have grease or oil on them

## Slide 48: NFPA 1911 Out of Service Criteria (Cont’d)
I. Braking Systems (Air) (Cont’d)
  Rotors and/or drums that are worn beyond manufacturer’s min. specifications
  Brake linings or pads worn beyond manufacturer’s min. specifications
  Air gauge or audio low-air warning device failure

## Slide 49: NFPA 1911 Out of Service Criteria (Cont’d)
J. Braking Systems (Hydraulic)
  Leaking brake fluid
  Brake shoes or disc brake pads that have grease or oil on them
  Braking systems not operational
  Braking systems that do not meet tests or standards
  ABS warning indicator (light) activated

## Slide 50: NFPA 1911 Out of Service Criteria (Cont’d)
J. Braking Systems (Hydraulic) (Cont’d)
  Parking (service brake) that does not meet tests or standards
  Brake warning light that is activated or brake pedal that falls away or drifts toward floor when brake pressure is applied
  Brake linings, pads, rotors, drums that do not meet manufacturer’s min. specifications
  Rotors and/or drums that are worn beyond manufacturer’s min. specifications

## Slide 51: NFPA 1911 Out of Service Criteria (Cont’d)
K. Fire pump system
  Pump will not engage
  Pump shift indicator does not function properly
  Pressure control system not operational
  Pump transmission components have a leak

## Slide 52: NFPA 1911 Out of Service Criteria (Cont’d)
K. Fire pump system (Cont’d)
  Pump operator’s panel throttle is not operational
  Pump operator’s engine speed advancement interlock is not operational

## Slide 53: NFPA 1911 Out of Service Criteria (Cont’d)
L. Aerial device systems
  Power takeoff (PTO) will not engage
  Stabilizer system is not operational
  Aerial device is not operational
  Hydraulic system components are not operational
  Cable sheaves that are not operational

## Slide 54: NFPA 1911 Out of Service Criteria (Cont’d)
L. Aerial device systems
  Cables are frayed
  Base and section rails show ironing beyond recommendations
  Aerial device is deformed
  Torque box fasteners and turntable fasteners broken or missing

## Slide 55: Recordkeeping
Maintenance Records
Operational Records

## Slide 56: Practical Application
Review and discuss the departments out of service criteria and the process to document and report the defect.
Notes: Explain the role of the driver in performing the vehicle check and the importance of keeping accurate and complete records. Review the forms required by the AHJ.