## Slide 1
Module
VI

## Slide 2: Module VI - The Vehicle
Goal
To have the participant understand physical forces which act upon vehicles and impact their handling. Study the various vehicle characteristics and how they impact both the physical forces acting on the vehicle and the manner in which the vehicle handles.

## Slide 3: Module VI - The Vehicle
Objectives
Understand the differences between various vehicle types.
Recognize how technology may assist drivers of emergency vehicles.
Identify vehicle components and features.

## Slide 4: Glossary of Terms
Ballast - Anything that is not secured and may become a projectile.
Sterile Cab - eliminating non-essential duties or activities such as; casual conversation, listening to music, eating, and cell phone use, and unnecessary conversation while the apparatus is responding in an emergency mode.

## Slide 5: Types of Emergency Vehicles

## Slide 6: Types of Ambulances
Type | Description | GVWR (lbs.)
Type I | a cab chassis furnished with a modular ambulance body | 10,001 – 24,000
Type I – AD | Type I with increased GVWR, storage, and payload | 14,001 or more
Type II | a long wheelbase van, with integral cab-body | 9,201 – 14,000
Type III | a cutaway van with integrated modular ambulance body | 10,001 – 14,000
Type III – AD | Type III with increased GVWR, storage, and payload | 14,001 or more

## Slide 7: Sterile Cab
A Research Study of Ambulance Operations and Best Practice Considerations for Emergency Medical Services Personnel recommends the securing of all items in the vehicle.
NFPA 1901 requires all equipment not required to be used during an emergency response to be contained in a bracket capable of containing its contents through a 9 g force in the longitudinal axis or a 3 g force in any other direction.

## Slide 8: Sterile Cab
Personal items such as keys and cellular phones as well as clipboards and portable radios are often left unsecure in the cab of emergency vehicles and are a real hazard to responders. These items are known as ballasts.

## Slide 9: Sterile Cab
The goals of a Sterile Cab include but are not limited to:
Minimize the use of communication devices (hands on and hands free)
No texting
No eating
Turn off music
Minimize casual conversations
Secure all equipment in the cab to 3 g compliance
Participant Manual
ACTIVITY

## Slide 10: Technology
Advances in technology have led to the development of a number of systems that may assist drivers and have improved safety on the roads.
  Autonomous Vehicle Technology
  GPS Monitoring Systems
  Forward Collision Warning Systems (CWS)
  Lane Departure Warning Systems (LDWS)
  Roll Stability Control Systems (RSC)
  Electronic Driver Monitoring/Feedback Systems
  Onboard Video Monitoring

## Slide 11: Five Levels of Automation
Level 0 – No Automation
Level 1 – Function Specific
Level 2 – Combined Function
Level 3 – Limited Automation
Level 4 – Full Automation

## Slide 12: Technology
Roll Stability control Systems (RCS)
  Level 1 Automation – Function Specific
  Automatically intervene if a high rollover risk is detected while driving

## Slide 13: Technology
Electronic Driver Monitoring/Feedback Systems Monitor:
Speed
G-forces
Fuel Consumption
Etc.

## Slide 14: Technology
Onboard Video Monitoring Systems
Continuous video monitoring
  May only record when activated
May have driving metrics similar to Driver Monitoring/Feedback Systems
May have driver audible warning signals
Provide learning and/or coaching opportunities

## Slide 15: Vehicle Features
Transmission
Automatic
Manual

## Slide 16: Automatic Transmissions
Lever Shift
R – reverse
N – neutral
D – drive
Use shift lever to change gears.

## Slide 17: General Information - Automatic
The display window should display the gear the transmission is in
Use arrow button or shift lever to change gears
Do not shift from neutral to drive or reverse at engine speeds above idle
Stop the vehicle completely before shifting from a forward to reverse or reverse to forward

## Slide 18: General Information - Automatic
Select drive for all normal driving conditions
The transmission will upshift and downshift automatically
Accelerator pedal position influences the automatic shifting
The lower the gear range, the greater the engine braking power

## Slide 19: General Information - Automatic
Use up or down arrow button on push button selector to reach the desired gear. On the lever shift selector, depress the override button and move the shift selector to the desired gear
Use neutral for parking and apply parking brake
Do not allow the vehicle to coast in neutral

## Slide 20: Manual Transmission

## Slide 21: Shifting Gears -UP
Release accelerator, push in clutch and shift into neutral at the same time
Release clutch
Let engine and gears slow down to the rpm required for the next gear
Push in clutch and shift to higher gear
Release clutch and press accelerator at the same time

## Slide 22: Shifting Gears -DOWN
Release accelerator, push in clutch and shift into neutral at the same time
Release clutch
Press accelerator, increase engine and speed to the rpm required in the lower gear
Push in clutch and shift to lower gear at the same time
Release clutch and press accelerator at the same time

## Slide 23: Special Vehicles

## Slide 24
Participant Manual
ACTIVITY