## Slide 1
Module
VII

## Slide 2: Module VII – Vehicle Dynamics
Goal
To have the participant understand the forces that act upon vehicles and how both vehicle design and physical forces affect handling.

## Slide 3: Module VII – Vehicle Dynamics
Objectives
Understand the physical forces that affect vehicle handling.
Recognize that vehicle characteristics influence the effect of physical forces on emergency vehicles.

## Slide 4: Vehicle Dynamics Overview
Driving Too Fast
Accelerating Too Quickly
Traction Control
Braking Too Hard
Brake Fade
Changing Direction
Traveling Through a Curve

## Slide 5: Physical Forces
Friction
Velocity
Momentum and Inertia
Centrifugal Force

## Slide 6: Physical Forces
Friction – resistance to motion between two moving objects that touch.
Tire/Road Friction
Brake Friction
Steering Friction

## Slide 7: Physical Forces
Velocity – speed
Acceleration (velocity increase)
Deceleration (velocity decrease)
Braking (velocity decrease)
Participant Manual
ACTIVITY

## Slide 8: Physical Forces
Momentum – is measured as the product of the object’s mass or weight times its velocity.
Inertia – the force it takes for a moving object to stay in motion in the same direction.

## Slide 9: Physical Forces
Centrifugal Force – the force caused by inertia, which tends to make a rotating body move away from the center of rotation.

## Slide 10: Physical Forces

## Slide 11: Vehicles in Motion
Sway (Roll)
Dive – Squat (Pitch)
Over steer (Yaw)

## Slide 12: Vehicles in Motion
Chassis in Motion
Controlling Motion
Weight Transfer

## Slide 13
Pitch is rotation around an axis running from the driver's left to right in a vehicle; thus the front pitches up and the rear down, or vice-versa.

## Slide 14
Yaw is rotation about an axis drawn from top to bottom, and perpendicular to the other two axes.

## Slide 15
Roll is rotation around an axis drawn through the body of the vehicle from rear to front in the normal direction of travel, or the direction the driver faces.

## Slide 16: Vehicle Characteristics
Total Weight and Weight Distribution
Suspension System
Braking System(s)
Rollover Awareness
HEIGHT: 8 ft. 11 in.
LENGTH: 20 ft. 6 in.
WEIGHT: 14,800 lbs

## Slide 17: Vehicle Characteristics
Total Weight and Weight Distribution
  Gross Axle Weight Rating (GAWR)
  Gross Vehicle Weight Rating (GVWR) or (GCWR)
  Weight Distribution – Horizontal and Vertical Centers of Gravity

## Slide 18: Vehicle Characteristics
Suspension System
  Axles
  Springs
  Wheels and Tires

## Slide 19: Braking Systems
Standard
Parking or Service
Auxiliary Braking Systems

## Slide 20: Standard

## Slide 21: Air Brake System
Foot Brake Valve
Front & Rear Axle Tanks
Main Air Supply Tank
Air Dryer
Compressor
Governor

## Slide 22: Braking Systems
Braking Systems
  Electronic Braking Control Systems (ECBS) brake by wire
  Anti-lock Braking Systems (ABS)
  Secondary or Auxiliary Braking Systems
    Driveline Retarder
    Compression or Engine Brake
    Exhaust Brake
    Automatic Transmission Retarder

## Slide 23: Braking Systems
Auxiliary brakes increase the life of brake linings
Some auxiliary braking devices should be shut off when the apparatus is being operated on slippery/wet surfaces
  Check your vehicle’s operation manual

## Slide 24: Vehicle Characteristics
Rollover Awareness
  Center of Gravity
  Road Conditions
  Seatbelts

## Slide 25: Static Stability Factor
This mechanism is the source of a well-known rigid vehicle Static Stability Factor:
SSF= ─
T
2h

## Slide 26: Stability Factor Calculation
T = 6’
Height | SSF
2’ | 1.5
3’ | 1.0
4’ | .75
5’ | .6
6’ | .5
7’ | .42
8’ | .375
9’ | .333
10’ | .3

## Slide 27: Weight Transfer
The amount of weight on your tire is what ultimately determines its traction limit. Too little weight and the rubber doesn’t stick to the road; too much weight causes it to stick too hard and creates excess heat

## Slide 28: Vehicle Balance and Traction Concepts
When the vehicle is in motion:
  Sudden steering, braking and/or acceleration change vehicle balance and traction dramatically
  Sudden loss of vehicle balance causes traction loss and traction loss compounds crash results

## Slide 29: Vehicle Balance and Traction Concepts
When brakes are applied:
  Weight or center of mass transfers to the front of the vehicle
  Causes a noticeable drop of the front of the vehicle and a rise in the rear
  Occupants feel a forward movement

## Slide 30: Vehicle Balance and Traction Concepts
When acceleration is applied:
  Weight or center of mass transfers to the rear of the vehicle
  Causes a noticeable rise to the front of the vehicle and a drop in the rear of the vehicle
  Occupants feel a rearward movement

## Slide 31: Vehicle Balance and Traction Concepts
When steering is applied:
  Weight or center of mass transfers to the front right or left of the vehicle
  Causes a noticeable drop and tilt of the front of the vehicle and a rise and tilt of the rear of the vehicle
  Occupants feel a movement forward to the corner of the vehicle

## Slide 32: Vehicle Balance and Traction Concepts
Key to vehicle operation:
  Smooth and efficient steering, braking, and accelerator movements
  Any abrupt movements or changes of the vehicle are transferred to the vehicle suspension and have a significant affect on the balance of the vehicle

## Slide 33: Vehicle Balance and Traction Concepts
Traction concerns:
  Stationary (Static) – A stationary vehicle parked on a flat surface with brakes set is an example of static traction. It has greatest resistance to movement. There is greater traction between a stationary wheel and a road than a sliding wheel and a road

## Slide 34: Vehicle Balance and Traction Concepts
Traction concerns:
  Rolling (dynamic) –There is more traction between a rolling and wheel and the road. This is why a driver needs to keep the wheels rolling and not lock the brakes when trying to steer or stop a vehicle

## Slide 35: Vehicle Balance and Traction Concepts
Traction concerns:
  Sliding – Traction between tires and the road does not remain constant. Sand, gravel or water on the road decrease the level of traction. As speed increases, traction between the tires and the road surface decrease. With the decrease traction, the possibility of skidding or sliding increases

## Slide 36: Matching Speed to Road Conditions
Slippery surfaces

## Slide 37: Matching Speed to Road Conditions
Curves

## Slide 38: Matching Speed to Road Conditions
Downhill grade

## Slide 39: Matching Speed to Road Conditions
Steep grade

## Slide 40: Warning
When descending grade, remember that frequent use of service brakes causes them to become hot, which results in a reduction of their stopping ability.

## Slide 41: Rollover Prevention
FEMA/USFA White Paper Findings
Driver error is a major factor in nearly all incidents
Majority are single vehicle crashes
Inexperience or lack of specific training is major factor
Failure to wear seat belts contributes to many fatalities

## Slide 42: Common Rollover Circumstances
Too much relative speed into curve or corner
Soft shoulder drop-off
Uneven surface drop-off and improper recovery

## Slide 43: Excessive Relative Speed
Vehicle speed measured at any MPH which is considered unsafe in relationship to your environment, road conditions, and your vehicle

## Slide 44: Rollover Prevention
Soft Shoulder Drop off
  Unpaved road or paved road w/unpaved shoulder
  Tires drop-off onto shoulder & may begin to sink
  Driver brakes abruptly
    Transferring considerable vehicle weight causing wheels to plow
    Slowing vehicle abruptly and sinking into soft shoulder

## Slide 45: Rollover Prevention
Uneven Surface Drop off and Improper Recovery
  Travel likely on road with an unpaved shoulder
  Driver drifts off of paved surface with right tires
  In an attempt to get vehicle back onto road surface, the driver over steers hard left

## Slide 46: Rollover Prevention
Body Roll
  The movement of the body & chassis onto the suspension & tires
  Dynamic weight transfer causes changes in the vehicle’s weight distribution on:
    Each axle
    Each tire
    Center of gravity

## Slide 47: Rollover Prevention
Causes of Body Roll
  Acceleration
  Water Slosh
  Steering motion
  Road configurations
  Driving thru a curve
  Tire sidewall flexibility
  Personnel moving inside vehicle

## Slide 48: Wear Seatbelts & Slow Down